| Risk Assessment – Specific Activity/Situation |  |
| --- | --- |
| Risk Assessment Reference No: | MO-29-10_19 |

| Workplace Activity: | Using petrol Leaf Blower | Date: | October 2019 |
| --- | --- | --- | --- |

| Persons at Risk- Affected by Activity: | Site Team | Number | 1 |
| --- | --- | --- | --- |
| Any Vulnerable Persons Affected by Activity: | Persons with restricted mobility | Number | TBC |

| Setting the Scene: Clearing playground, pathways and borders of fallen leafs with a petrol blowing machine. |
| --- |
| Potential Hazards | Assessment of Risk |
| Ref. |  | Low | Med | High |
| 1. | Physical injury caused by manual handling |  | X |  |
| 2. | Slips and trips on uneven ground or algae covered floor surfaces |  | X |  |
| 5. | Fire caused when filling fuel/static electricity | X |  |  |
| 6. | Injury through flying stones or sharp objects such as plastic toys |  |  | X |
| 8. | White knuckle syndrome, vibration white finger (VWF) or Secondary Raynaud's disease | X |  |  |
| 9. | Noise induced hearing loss |  | X |  |
| 10. |  |  |  |  |

Existing Control Measures

1, MO attend manual handling training every 3 years. small quantities of fuel are stored in the external storeroom – 5 litre containers. MO is advised to inform their immediate line manager if they suffer from MSD’s.

2. MO will check the site prior to beginning activity to assess conditions. The site will be kept tidy and clear of loose materials and tools MO to wear good quality safety boots with non-slip sole PPE will be worn including safety gloves, goggles and safety boots. The MO will not use the leaf blower during normal school hours.

5. Fuel must be in approved containers, up to 5 litres in plastic and 10 litres in metal jerry can. Refuel only when machine has cooled in a ventilated area. Refuelling to occur 3 metres away from ignition source, work area and water course or drain. Spill kit must be present in area used when refilling. All fuel caps are kept securely in place except during the refuelling operation. Excess fuel is stored in the secure external storeroom – no more than 5 litres kept in storage. Leaf blower is stored upright when not in use to reduce risk of spillages. Flammable signs are displayed outside store room. No smoking is permitted on site.

6. Other pedestrians should be at least 5 metres away from the blower in operation. The working area is taped or coned off to prevent members of the public from being endangered. MO should use a visor or goggles kite marked for impact protection. Any machine guards present must be in place and in good working order MO will carry out visual inspection of area to be worked in prior to commencing the blowing process. Any small toys or obvious stones will be removed from the area. Leaf blower will only be used in daylight hours.

8. Strimmer will be well maintained and vibration-dampeners inspected before operation. Manufacturer’s instructions will show maximum usage times for an optimally maintained strimmer. Take regular breaks e.g. 10 minutes between tank fills and 30 minutes between 3 tank fills.

9. Always were hearing defenders when using the strimmer.

| Initial Assessment of Overall Risk | Low |  | Medium |  | High | X |
| --- | --- | --- | --- | --- | --- | --- |

| RISK RATING = SEVERITY x LIKELIHOOD |
| --- |
| Rating | SEVERITY of injury/disease | LIKELIHOOD of occurrence |
| HIGH | Fatality; major injury or illness causing long term disability | Certain or near certain to occur |
| MEDIUM | Injury or illness causing short term disability | Reasonably likely to occur |
| LOW | Other injury or illness | Unlikely to occur |

| ADDITIONAL CONTROL MEASURES - (IF APPLICABLE) | PERSON RESPONSIBLE FOR IMPLEMENTATION | COMPLETION DATE |
| --- | --- | --- |
| Check that the site team have been issued with gloves, safety glasses and helmets for use when using the strimmer. | Site Manager |  |
| All site team using this equipment must read the risk assessment and method statement (see additional information) prior to use. | Site Manager |  |

| RESIDUAL ASSESSMENT OF OVERALL RISK | LOW |  | MEDIUM | X | HIGH |  |
| --- | --- | --- | --- | --- | --- | --- |

Note:	Re-assessment required if overall residual risk is High

ADDITIONAL INFORMATION: (Notes, comments, further details, outline procedures, safe systems of work, standards, drawings, etc.)

Pre-Operational Check: Locate and ensure you are familiar with all machine operations and controls. Check for loose/ missing nuts, bolts and screws. Tighten and/or replace as needed. Inspect fuel lines, tank and area around carburettor for fuel leaks. Do not operate if leaks are found. Ensure all guards are fitted, secure and functional. Identify ON/OFF switch and emergency stop button. Ensure all other people are clear of the immediate work area. Safe Operation: 1. Ensure that no person or animal is endangered when operating equipment. 2. When you start up the machine, listen for unusual noises or vibrations. 3. When starting, stand the blower upright on a level surface. Check that the blower pipe is not blocked by the ground or by any objects. 4. Allow the blower to warm up at fast idle for a few minutes before using. 5. Keep a firm grip. Hold handle with fingers together encircling handle. Maintain a straight wrist position. Avoid using your wrist in a bent, extended or twisted position. 6. Make sure the muffler side of the engine is away from your body to avoid burns. 7. Maintain a proper balance and secure footing. Do not work on slippery, uneven or unstable surfaces. Do not work in off positions or on ladders. 8. Take wind conditions into account. Avoid open doors and windows. 9. Minimise dust by using blower at lower speed. 10. Always keep exhaust area clear of flammable debris. 11. Disconnect spark plug wire before you work on the unit or leave unattended. 12. Allow the engine and muffler to completely cool before refueling or performing any maintenance work. 13. Ensure good housekeeping practices are in place to minimize waste build-up. Storage & Maintenance: 1. Turn off the fuel supply and disconnect spark plug when work completed. 2. Remove any foreign material from in and around engine. 3. Allow to cool down before packing away.

| Risk Assessment Circulation List (tick box) |
| --- |
| Employees |  | Management |  | Contractors |  |
| Other – Specify: |  |  |  |  |  |
| Signature of responsible person: | Date: |
| Assessor: | Adele Partridge, CMIOSH MIIRSM | Signature: |  |
| Date Assessed: | October 2019 | Review Date: | October 2019 |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |