| Risk Assessment – Specific Activity/Situation |  |
| --- | --- |
| Risk Assessment Reference No: | MO-12-10_19 |

| Workplace Activity: | Using Jet Washer equipment | Date: | October 2019 |
| --- | --- | --- | --- |

| Persons at Risk- Affected by Activity: | Facilities Maintenance Team | Number | 4 |
| --- | --- | --- | --- |
| Any Vulnerable Persons Affected by Activity: | - | Number | - |

| Setting the Scene: Site Maintenance team using Jet Wash cleaning equipment to 1. 2. 3. |
| --- |
| Potential Hazards | Assessment of Risk |
| Ref. |  | Low | Med | High |
| 1. | Eye damage caused by jet wash splashing stones on the floor | X |  |  |
| 2. | Injury/electrocution from the failure of equipment (coming into contact with water) or damage to electrical wires |  | X |  |
| 3. | Trips caused by trailing wires |  | X |  |
| 4. | Slips caused by wet ground | X |  |  |
| 5. | Burns caused by heat of water | X |  |  |
| 6. | Exposure to dangerous fumes (petrol equipment) | X |  |  |
| 7. | Irritant to employees breathing in mist caused by spray | X |  |  |

Existing Control Measures

1 Always wear safety glasses Never aim pressure hose in direction of spectators Warn bystanders prior to starting machine

2. Check lead for cuts, breaks prior to starting electric pressure cleaner Ensure electrical test tag is current and in date Ensure circuit breaker of power source is functioning correctly Portable Appliance Tests are carried out on all machines by qualified engineers during every repair or annually if no fault has been recorded.

3. Clear work area of potential obstacles prior to commencing work Be aware of the positioning of both the pressure and garden hoses to avoid getting your feet tangles in either Operatives to ensure that electrical cables do not become raised from the floor during operation.

4. Wet surfaces may become slippery and us such extreme caution should be used • Never operate from dangerous areas such as ladders, walls etc

5. Wear safety gloves to protect hands from hot parts • Allow machine time to cool down after use prior to moving

6. Never use petrol pressure cleaner in confined spaces • Always ensure adequate ventilation prior to use

7. Low-level health surveillance is carried out for health hazards associated with chemicals used alongside Jet Wash equipment. CoSHH Assessments are completed.

| Initial Assessment of Overall Risk | Low | x | Medium |  | High |  |
| --- | --- | --- | --- | --- | --- | --- |

| RISK RATING = SEVERITY x LIKELIHOOD |
| --- |
| Rating | SEVERITY of injury/disease | LIKELIHOOD of occurrence |
| HIGH | Fatality; major injury or illness causing long term disability | Certain or near certain to occur |
| MEDIUM | Injury or illness causing short term disability | Reasonably likely to occur |
| LOW | Other injury or illness | Unlikely to occur |

| ADDITIONAL CONTROL MEASURES - (IF APPLICABLE) | PERSON RESPONSIBLE FOR IMPLEMENTATION | COMPLETION DATE |
| --- | --- | --- |

| RESIDUAL ASSESSMENT OF OVERALL RISK | LOW | X | MEDIUM |  | HIGH |  |
| --- | --- | --- | --- | --- | --- | --- |

Note:	Re-assessment required if overall residual risk is High

ADDITIONAL INFORMATION: (Notes, comments, further details, outline procedures, safe systems of work, standards, drawings, etc.)

This instruction should be read in conjunction with the Risk Assessment procedure for a Pressure Washer. GENERAL SAFETY • Safety glasses, gloves, safety footwear and Hi-Vis Jacket are recommended under operating conditions • Close fitting protection clothing must be worn • Hearing protection must be considered when using this machine POTENTIAL RISKS • Users/Clients should review the risk procedure document for this machine • Care must be taken to avoid flying debris and cuts and abrasions from spray contact or back spray • Electrocution can occur from power faults, faulty equipment, incorrect use or spraying electrical power sources • Brace correctly and move carefully to avoid trips or falls. TRANSPORT OF PRESSURE WASHER • Ensure unit is firmly tied down on transport vehicle without damaging mechanical components or hose • Make sure hoses are not kinked OPERATING CONDITIONS • Before use, check power cord, extension lead, hoses, sockets and power outlet for damage • DO NOT OPERATE IF ANY FAULTS FOUND • Make sure electrical lead test tags are up to date • Ensure no other persons are in the immediate work area • Only use pressure washer when hand held and never leave washer when it’s running • Ensure electrical lead and hose movement is not impeded while working • DO NOT OPERATE WASHER UNTIL WATER SUPPLY IS ATTACHED AND RUNNING • DO NOT POINT HOSE AT ANY PERSON INCLUDING THE OPERATOR • DO NOT LOCK TRIGGER IN THE ‘ON’ POSITION • Cleaned surface may be damaged if nozzle is too close to that surface • Monitor work area to ensure no person is in a position to be injured by dislodged material • IF ANY PERSON ENCROACHES INTO WORK AREA, IMMEDIATELY RELEASE TRIGGER AND STOP WORK • Continually check that electrical lead is not lying in water • When finished, release trigger and place nozzle on ground pointing away from machine and people • Turn cleaner off at the machine • Turn off water supply and disconnect from tap • Coil power lead and hose and position to one side • Store unit in an appropriate location INSPECTION AND MAINTENANCE • Always check power cord, extension lead, hoses, sockets and power outlet for damage • Check that electrical lead and plugs are not wet • Make sure electrical lead test tags are up to date • Make sure hose is not kinked The above instructions must be followed at all times If any of the instructions are not possible, contact the site supervisor for an assessment of any safety requirements

| Risk Assessment Circulation List (tick box) |
| --- |
| Employees |  | Management |  | Contractors |  |
| Other – Specify: | MO |  |  |  |  |
| Signature of responsible person: | Date: |
| Assessor: | A Partridge | Signature: |  |
| Date Assessed: | October 2019 | Review Date: | October 2020 |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |