| Risk Assessment – Specific Activity/Situation |  |
| --- | --- |
| Risk Assessment Reference No: | MO---21-10_19 |

| Workplace Activity: | Use of Ladders & stepladders | Date: | October 2019 |
| --- | --- | --- | --- |

| Persons at Risk- Affected by Activity: | Site Manager, cleaners | Number | 4 |
| --- | --- | --- | --- |
| Any Vulnerable Persons Affected by Activity: | Persons with restricted mobility | Number | TBC |

| Setting the Scene: Maintenance officers use ladders for a variety of tasks each day. Most working at height tasks are performed outside of normal school hours, except for any urgent maintenance tasks that are required due to failure of equipment (such as overhead projectors). Cleaners might use step ladders for cleaning tasks above head height. Site team may need to access Loft’s or high level areas of the school. |
| --- |
| Potential Hazards | Assessment of Risk |
| Ref. |  | Low | Med | High |
| 1. | Falls from height resulting from: Overstretching Unbalance Failure of ladders through incorrect set up Slippery floor Unauthorised use of ladder (i.e. pupils) | X |  |  |
| 2. | Materials or equipment falling from ladder | X |  |  |
| 3. | Ladder obstructing pedestrian areas, resulting in collision. |  | X |  |

Existing Control Measures

1. Do not carry out any task which requires access to more than 3 steps, unless a separate work at height risk assessment has been completed. Ladders are only used for short duration work (less than 30 minutes) Only one person should ascend the stepladders / ladders at any one time Always secure stepladders and ladders on stable flat ground, ensuring ground area around the base is kept clear. Staff are only permitted to use the ladder if they have received instruction. Three points of contact should be maintained with the stepladder/ladder whilst working at height. When using ladders members of staff do not work on top 3 rungs or top 2 steps of stepladders. Visual inspection of stepladders/ladders for defects before each use. Annual formal inspection carried out with records stored in MO’s files. Inspected ladders will be labelled to show the date of last inspection. Any damage to ladders should be reported to the site team and the ladder is not to be used Staff must wear flat foot wear if using a ladder (no flip flops or mules) Stepladders must be fully open when in use, stay bars are to be locked in place

2. Ladders are only used for light work and not for work that involves carrying heavy or awkward items. Tools should be carried on a tool belt or secured to staff whilst climbing the ladders Equipment should not be carried whilst climbing the ladder and should be raised to height by being passed up by an assistant A safety zone should be established around the base of the ladder. The safety zone should restrict access to any area where materials or equipment may fall into.

3. Ladders are removed to storage at the end of each working day to ensure that unauthorised access to roof etc by others, particularly pupils, is prevented.

| Initial Assessment of Overall Risk | Low |  | Medium |  | High |  |
| --- | --- | --- | --- | --- | --- | --- |

| RISK RATING = SEVERITY x LIKELIHOOD |
| --- |
| Rating | SEVERITY of injury/disease | LIKELIHOOD of occurrence |
| HIGH | Fatality; major injury or illness causing long term disability | Certain or near certain to occur |
| MEDIUM | Injury or illness causing short term disability | Reasonably likely to occur |
| LOW | Other injury or illness | Unlikely to occur |

| ADDITIONAL CONTROL MEASURES - (IF APPLICABLE) | PERSON RESPONSIBLE FOR IMPLEMENTATION | COMPLETION DATE |
| --- | --- | --- |
| Check that there is a suitable selection of ladders available for the tasks to be carried out (see Additional Information). | Site Team |  |
| Create an inventory of all ladders on school property – display in poster on how carry out a safety check on ladders. | Site Team |  |

| RESIDUAL ASSESSMENT OF OVERALL RISK | LOW |  | MEDIUM |  | HIGH |  |
| --- | --- | --- | --- | --- | --- | --- |

Note:	Re-assessment required if overall residual risk is High

ADDITIONAL INFORMATION: (Notes, comments, further details, outline procedures, safe systems of work, standards, drawings, etc.)

See separate risk assessment for Access to Flat Roof – MO-18-10_19 List the names of persons who have attended Working at Height Training within the last 3 years here: Stepladders/ladders must be to BSEN131 Professional standard. Any ladders which do not show a suitable label will be disposed of.

| Risk Assessment Circulation List (tick box) |
| --- |
| Employees |  | Management |  | Contractors |  |
| Other – Specify: |  |  |  |  |  |
| Signature of responsible person: | Date: |
| Assessor: | Adele Partridge, CMIOSH MIIRSM | Signature: |  |
| Date Assessed: | October 2019 | Review Date: | October 2020 |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |