| Risk Assessment – Specific Activity/Situation |  |
| --- | --- |
| Risk Assessment Reference No: | M0-03-10_19 |

| Workplace Activity: | Machine scrub floors | Date: | October 2019 |
| --- | --- | --- | --- |

| Persons at Risk- Affected by Activity: | Maintenance Officers & Cleaners using equipment; school staff in building | Number | 23 |
| --- | --- | --- | --- |
| Any Vulnerable Persons Affected by Activity: | People with existing musculoskeletal injury | Number | TBC |

| Setting the Scene: Electronic floor scrubbers are used to clean hard floor surfaces in corridors and the main hall. Equipment is owned and maintained by local authority departments, though used by staff located in the school. WBC contract cleaners are trained to use the equipment by their employer. The equipment is generally used no more than once per week, outside of normal school hours. In depth school cleaning is carried out during school holidays, reducing risk of injury to other staff. |
| --- |
| Potential Hazards | Assessment of Risk |
| Ref. |  | Low | Med | High |
| 1. | Various injuries from slips, trips and falls from trailing cables |  | X |  |
| 2. | Various injuries from slips, trips and falls from wet floors |  |  | X |
| 3. | Electrical shock due to adding cleaning chemicals to machine – substances coming into contact with electricity. | X |  |  |
| 4. | Back strain from moving the machine and changing cleaning pads |  | X |  |
| 5. | Irritation caused by handling cleaning solutions. | X |  |  |

Existing Control Measures

1. Warning signs are to be placed in the appropriate areas when machine is in operation. Staff are to use the nearest socket. Cables should not stretch across corridors if possible.

2. Cleaning operation is done outside of normal school hours. Wet floor signs are erected during cleaning operation and will be removed once floor surface is dry. Additional signage will be displayed on doors leading to the corridor/main hall, to warn pedestrians that floor cleaning is in operation. Staff carrying out cleaning operation must wear flat shoes with non-slip soles, to reduce risk of slipping.

3a. Only staff trained to prepare and use equipment will be authorised to operate machine. Users are to visually check the equipment before each use. The owner of the equipment is responsible for PAT Inspections. Maintenance officer checks that PAT label is present and in-date during monthly inspection checks.

4. Staff are to seek assistance for heavy or awkward lifts if suffering from existing musculoskeletal conditions. Manual handling training is provided to all users (every 3 years) If machine is to be used in multi-floor building, the lift will be used to move equipment between floors). The best techniques for manoeuvring equipment will be discussed during Manual Handling training. Any staff member suffering from a bad back must tell their supervisor so that alternative control measures can be implemented.

5. CoSHH assessments are written to include hazards associated with use of cleaning substances. Assessments filed in Cleaners cupboard. Cupboard is locked during school hours. Staff are reminded to inform their supervisor if there are any changes to skin associated with use of cleaning chemicals, ie. dry patches, irritation.

| Initial Assessment of Overall Risk | Low | x | Medium |  | High |  |
| --- | --- | --- | --- | --- | --- | --- |

| RISK RATING = SEVERITY x LIKELIHOOD |
| --- |
| Rating | SEVERITY of injury/disease | LIKELIHOOD of occurrence |
| HIGH | Fatality; major injury or illness causing long term disability | Certain or near certain to occur |
| MEDIUM | Injury or illness causing short term disability | Reasonably likely to occur |
| LOW | Other injury or illness | Unlikely to occur |

| ADDITIONAL CONTROL MEASURES - (IF APPLICABLE) | PERSON RESPONSIBLE FOR IMPLEMENTATION | COMPLETION DATE |
| --- | --- | --- |
| Ensure the Floor buffer Safety Procedure is displayed for cleaners/MO to read. Obtain signatures to show that users are aware of the hazards, control measures and routine maintenance procedures. | SMO |  |

| RESIDUAL ASSESSMENT OF OVERALL RISK | LOW |  | MEDIUM |  | HIGH |  |
| --- | --- | --- | --- | --- | --- | --- |

Note:	Re-assessment required if overall residual risk is High

ADDITIONAL INFORMATION: (Notes, comments, further details, outline procedures, safe systems of work, standards, drawings, etc.)

PRE-OPERATIONAL SAFETY CHECKS Conduct a pre-start inspection of the buffer and power cord/plug. Do not use if damaged. Bend knees to lessen pressure on lower back when changing pads and moving machine. Move the machine on its wheels. Keep fingers away from attachment area and moving parts. Adjust the handle to suit the user. The preferred height is the handle bar at lower groin level with arms near fully extended. Secure handle in required position. Rotate tasks with team members to reduce fatigue. Note the position of any electrical outlets or cords. Keep outlets dry and buffer clear of cord. Visually inspect floor to be cleaned. Only clean floors in good condition as lifted coverings may cause the machine to catch. Do not clean damaged floor areas. Buff designated floor surfaces only. Older floors may contain asbestos and may be unsuited to buffing. OPERATIONAL SAFETY CHECKS Place cleaning sign out. Be aware of any pedestrians. Keep all shoe laces tied and clear of rotating pads. Secure any loose clothing/jewellery. Wear proper footwear to prevent slipping. Use PVC gloves when handling chemicals. Make sure you and the plug are clear of any water. Do not run over cord when using machine. Maintain some slack in the cord to avoid over stretching the cord and pulling it from the power socket, damaging the power point and/or the buffer machine plug. Be aware of your surroundings. Make sure the path is clear before moving or using the machine. On some buffers the on/off switch is also the activation switch, others have a separate switch. Make sure switch is in off position before turning power on. Use the handle bar control to operate the machine. Machine is self-propelled. Take a balanced stance before turning power on and ensure machine is level so it will not grab and spin. ALWAYS USE TWO HANDS to control buffer. Be aware that machine may have a jerking motion if not used properly. Avoid reversing machine and walking in front of it. Rotate or share large/long buffing tasks to prevent muscle fatigue from vibration, grip tension and shoulder/back loading. Disconnect from power when unattended or changing pads. Take care to prevent fingers being sandwiched in fittings. Make sure you, the plug and cord are clear of any water before turning machine off. HOUSEKEEPING ( Remove cleaning pads after use. Dispose of in industrial bin; or rinse and allow to dry. Do not store machine resting on drive pad. Remove drive pad or store horizontally. ( Hoses and electrical leads should be coiled and tied for protection against damage and for ease of storage. All attachments should be removed and stored suitably e.g. on a shelf or in boxes.

| Risk Assessment Circulation List (tick box) |
| --- |
| Employees |  | Management |  | Contractors |  |
| Other – Specify: |  |  |  |  |  |
| Signature of responsible person: | Date: |
| Assessor: | Adele Partridge, CMIOSH MIIRSM | Signature: |  |
| Date Assessed: | October 2019 | Review Date: | October 2020 |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |

| RISK ASSESSMENT REVIEW - COMMENTS Date: |
| --- |
| Reason for Review |
| Reviewed By: |  | Signature: |  |